## Slide 1
“Commercial Biomass Utilization Today”

## Slide 2: Rio Bravo Rocklin
June 26, 2024
Total | Weekly Avg.
$39,472.00 | $4,934.00
Notes: Welcome. Introductions.

## Slide 3: Location: Lincoln, CA (near Sacramento)   Technology:CE/Lurgi Circulating Fluidized Bed Boiler, MHI turbine, Brush Electric Machines generator   Fuel(s): Biomass: 20% urban/agricultural wood, 80% agricultural/forestry wood (2017-2027 HHZ)   In-Service Date: May 1989   Capacity: 24.4 MW   Output: 5-year Power Purchase Agreement with SCE, 5-year extension expires 2027   Ownership: IHI Power Generation Corp. 50% North American Power Group 50%   Operator: IHI Power Services Corp.
Contact Information:
Jared Pate, Plant Manager
Alana Hodges, Admin.
(916) 645-3383
Address:
3100 Thunder Valley Court
Lincoln, CA 95648
Rio Bravo Rocklin
Notes: Rio Bravo Rocklin. Our current PPA runs to 2027.

## Slide 4
Chart: Renewables - Capacity Factor
| Geothermal | Hydroeletric | Other Biomass | Solar PV | Solar Thermal | Wind | Biomass Wood | Rio Bravo Rocklin
2011 | 0.715 | 0.458 | 0.642 | 0.19 | 0.239 | 0.321 | 0.596 | 0.8665
2012 | 0.683 | 0.396 | 0.633 | 0.204 | 0.236 | 0.318 | 0.613 | 0.8272
2013 | 0.718 | 0.388 | 0.623 | 0.245 | 0.174 | 0.324 | 0.59 | 0.8706
2014 | 0.72 | 0.372 | 0.627 | 0.256 | 0.183 | 0.34 | 0.6 | 0.888
2015 | 0.719 | 0.357 | 0.626 | 0.255 | 0.217 | 0.322 | 0.593 | 0.8688
2016 | 0.716 | 0.382 | 0.627 | 0.25 | 0.221 | 0.345 | 0.583 | 0.7888
2017 | 0.732 | 0.43 | 0.618 | 0.256 | 0.218 | 0.346 | 0.602 | 0.7659
2018 | 0.76 | 0.419 | 0.618 | 0.251 | 0.236 | 0.346 | 0.606 | 0.8237
2019 | 0.696 | 0.412 | 0.625 | 0.243 | 0.212 | 0.344 | 0.59 | 0.7875
2020 | 0.691 | 0.407 | 0.625 | 0.242 | 0.206 | 0.353 | 0.578 | 0.8265
Notes: How we compare to the other renewables. Compare to solar and wind. Compare to other biomass plants.

## Slide 5
Boiler
Fuel Reclaim
Fuel Storage
Fuel Receiving
Rio Bravo Rocklin
Notes: Aerial view of the plant.

## Slide 6: Biomass Power Plant System
Low Pressure Feed Water Heater
Deaerator
Feed Water
Pump
Blow Down Cooler
Gland Steam Condenser
Steam Jet Air Ejector
Condenser
Condensate
Pump
Condenser
Turbine Generator
Spray Water
Condenser
Main Steam
Circulating
Water Pump
Cooling Tower
Attemperator
Steam
Drum
Combustor
Backpass
Multiclone
Electrostatic Precipitator
ID Fan
Secondary Fan
Primary Fan
Upper
Air
Fly Ash Silo
Finishing
Bottom
Ash
Lower
Air
Metering
Bin
Truck Dumper
Surge Storage Pile
Reclaim Pile
Over Pile Flight Reclaimer
Stationary Stacker Belt Conveyor
Screen Belt Conveyor
Boiler Feed
Belt Conveyor
Cyclone
Primary
Economizer
Superheater
Stack
Screw Conveyor
Screw Feeder
Ash Conveyor
Biomass wood fuel
Circulated Fluidized Bed Boiler
Seal Pot
Transformer
Rotary
Feeder
Wood Fuel
NH3
NH3
NH3
NH3
Boiler type: CFB
Fresno, Rocklin

## Slide 7: Biomass Power – A Green Energy Source
Biomass power plants combust low-value wood material to produce electricity
Biomass Fuels are sustainable
  Forest waste such as saw mill residue, small trees and undergrowth cleared from forests for fire suppression and growth enhancement
  Agricultural wood such as orchard pruning / removals, rice hulls, fruit pits, etc.
  Urban “secondary material” wood such as construction wood scraps, broken pallets, clean used wood from factories and tree trimmings
Notes: What is biomass? Biomass to us is low-value wood material that has no other real use.

## Slide 8: Rio Bravo Rocklin 220,000 tons annually
Notes: One plant utilizes enough material in a year to fill the Rose Bowl. Overall, CA biomass utilizes 25 Rose Bowls. CA has an excess organics problem and biomass power is part of the solution.

## Slide 9: EMISSIONS REDUCED ANNUALLY FROM BIOMASS FACILITIES
Springsteen B, Christofk T, York R, Mason T, Baker D, et al. 2015. Forest biomass diversion in the Sierra Nevada: Energy, economics and emissions. California Agriculture Journal July-September 142-149.
Notes: The Placer County Air Pollution Control District participated in a study that compared the emissions from open pile burning and biomass energy
Open pile burning of biomass waste adversely impacts regional air quality and human health through release of various air pollutants – including:
  fine particulate matter (PM2.5)
  carbon monoxide (CO)
  nitrogen oxides (NOx)
  volatile organic compounds (VOCs)
  air toxics
  greenhouse gases of carbon dioxide (CO2)
  short-lived climate pollutants of methane and black carbon.
As an alternative to open pile burning, use in existing biomass power plants results in reductions of greater than 99% for PM2.5 and black carbon, 95-99% for CO and VOCs (including methane), 40-70% for NOx, and 30% for CO2(e).
These benefits have been conclusively demonstrated in numerous peer-reviewed comprehensive lifecycle assessments (Springsteen et al. 2015, Springsteen et al. 2011, Lee et al. 2010, Jones et al. 2010, Moyer and Pont 1997).
Reductions result from a combination of:
  utilization of wastes in power plants with efficient emissions control technology;
  negligible emissions from well controlled and efficient processing and transport equipment and engines; and
  production of renewable energy from wastes and that replace nonrenewable fossil fuel-generated energy.

## Slide 10
3100 Thunder Valley Ct.
Lincoln, CA 95648
Chris Quijano
cquijano@rbrocklin.com
Notes: Thank you. Proceed with tour, come back for questions.

## Slide 11: HL Power / Honey Lake Power
Placer County Water Agency
Biomass Supply Symposium
June 26,2024

## Slide 12: HL Power / Honey Lake Power

## Slide 13: Plant Overview - Personnel
  28 Greenleaf Power / HL Power Personnel
  1 Plant Manager
  1 Operations Supervisor
  1 Maintenance Supervisor
  1 Fuel Manager
  1 Operations and Maintenance Coordinator (OMC)
  4 operations teams on 12 hour rotating shifts—1 Supervisor, 1 Control Room Operator, 1 Auxiliary Operator, 1 Dozer Operator
  5 Team Members - 2 Millwrights, 1 IC/E, 1 Diesel Mechanic, 1 Ash Truck Driver / Utility Maintenance
  1 Scalehouse Weighmaster
  1 Administrative Assistant

## Slide 14: Plant Overview – Equipment (Motorhead Slide)

## Slide 15: Plant Overview - Production
In Service Since 1989
Production Capacity – 35.5 MW Gross / 30 MW Net
Parasitic Load – 2.5 MW
Geothermal Supplement
  5,000 Foot Deep Geothermal Well / BLM Lease
  Reinjection Well – Zero Drawdown to Resource, 35 Years
  Pre-Heats Steam-Water to 273 Degrees

## Slide 16: Fuel Procurement
  BioRAM Power Purchase Agreement
    26 MW Contract Production
    80% Sustainable Forest Management Sourced Fuel
    60% High Hazard Zone Sourced Fuel
  Plant Requirements
    Approximately 180,000 BDT / Year
    580 BDT / Day
    13,850 Chip Trucks / Year
    55 Chip Trucks / Business Day
    90 to 120 Days of Inventory at Year End (Winter Period)

## Slide 17: Fuel Procurement – Landowners / Suppliers
  Industrial Timberland Owners
    Collins Pine Company / TWC
    W.M. Beaty & Associates Managed Lands
    Sierra Pacific Industries
  Federally Managed Timberlands
    US Forest Service
    Bureau of Land Management
    National Park Service
  Various Non-Industrial Timberland Owners
  20-25 Timber Operators on a Yearly Basis
  30-40 Chip Trucks on a Yearly Basis

## Slide 18: Fuel Procurement – Facilitators
  Cal Fire
  US Forest Service
  Natural Resource Conservation Service
  Fire Safe Councils
    Lassen Fire Safe Council
    Plumas County Fire Safe Council
  Resource Conservation Districts
    Honey Lake Valley Resource Conservation District
    Pit Resource Conservation District
    Feather River Resource Conservation District

## Slide 19: Fuel Procurement – Treated Acres
Biomass Fuel Sources
  Processed Urban / Greenwaste – 8%
  Agricultural Residuals – 8%
  Sawmill Residuals – 10%
  Forest Biomass – 74% = 133,000 BDT
Approximate Treated Acres Facilitated
  Hazardous Fuel Reduction Projects
    80% of Forest Biomass = 106,000 BDT @ 10 BDT / Acre
      10,600 Acres Treated
  Timber Harvest Operations – Tops and Some Biomass Removal
    20% of Forest Biomass = 26,600 BDT @ 5 BDT / Acre
      5,320 Acres Treated
  Total Yearly Acres Treated = Approximately 16,000 Acres

## Slide 20: Fuel Procurement – High Hazard Zones

## Slide 21: Fuel Procurement – 50 Mile Radius
SRM

## Slide 22: Fuel Procurement – Hog, Sheep and Dixie Fires

## Slide 23: Fuel Procurement – Opportunities
  Grants for Landowner Assistance
  Grants for Transportation Assistance
  Grants for Facility Assistance
  Landscape Scale Projects
  Cull Logs

## Slide 24: Family Procurement – Opportunities

## Slide 25
Jim Turner
Director of Operations
Phone: (530) 355-9377
TahoeForestProducts.com
jturner@TahoeForestProducts.com
3736 Vista Grande Blvd., Carson City, NV 89705

## Slide 32
Promoting Healthy Forests
Tahoe Forest Products is constructing a commercial sawmill in Carson City, NV to provide responsible processing of harvested and salvaged local timber.
SCAN THE QR CODE TO LEARN MORE