## Slide 1
“Where the Biomass might go Tomorrow”

## Slide 2
Martin Twer
Biomass Program Director

## Slide 4: The future of Community Scale biomass conversion to electricity
The Biomass Supply Symposium
June 26, 2024

## Slide 5: The Existing Forest Biomass Infrastructure
6 Forest Biomass plants consume roughly 863,000 BDT of Biomass, 80% of which is forest biomass (690,000 BDT), under BioRAM contracts, producing approximately 154 MW with PPA contracts in place through 2027 to 2032. (Note: at least one of the facilities may need to terminate early due to difficulty accessing forest biomass waste). *Four of the facilities could each take 40-50 k more BDT per year if more support was given (totaling 160,000-200,000 BDT).
6 Forest Biomass plants that are managed by Sierra Pacific Industries, who use power onsite and sell power to various parties that gross 124 MW of production (not all is used on the grid). These plants process approximately 912,000 BDT of mill residue and SPI land clearance biomass. SPI has no additional capacity that we know of for non-SPI biomass.
2 Forest biomass plants at other forest products businesses using 255,000 BDT of mill residue and commercial lands biomass that produce 43 MW (not all is used on the grid), and have no additional capacity that we know of for offsite biomass.
4 Shuttered or idle facilities that are currently being recommissioned and anticipate using 450,000 BDT of forest biomass annually, for a total of approximately 45 MW of power.
1 BioMAT forest biomass plant online that uses 32,000 BDT of biomass waste from commercial lands and produces 5 MW with no additional capacity that we know of for offsite biomass.

## Slide 6: Concerns about current Fleet; Some real, Some imagined, All very Political
Calling the fleet “combustion facilities” and what that means
Air emissions at large scale facilities; its physics
What we are regulating at local air districts; Criteria pollutants, NOx, PM, CO, SO2 and VOC
Also local air districts regulate hazardous air pollutants (HAP)
Local Air Permit Processes and Violations
Current advanced emissions control technologies; including promising ceramic filtration
Start up/shut down and emergency power sources

## Slide 7: Air Quality And Small Scale Combustion
Smaller Scale means less emissions
Current emission control devices keep emissions low
Clean forest materials do not produce toxics as can be the case with treated wood
Placement in rural locations away from population centers
Physics: less is less
Ceramic Filtration is a Game Changer
Operates efficiently across a wide temperature range (350F to 850F), with low maintenance and operational costs.
Modular design with a small footprint, ideal for various facility sizes and space constraints.
Achieves >99.99% dust removal and >90% reduction in multiple pollutants, ensuring compliance with environmental regulations.
Effective for gasification, pyrolysis, and combustion technologies, with over three decades of success in the glass kiln industry.

## Slide 8: Community Scale and Microgrid Use of Biomass to Electricity (under 10 MW projects)
Communities prone to fire in forested communities
Generally in air basin attainment areas
Need jobs
Transmission/distribution network is outdated
Power shutoff concerns have been ameliorated by placement of fossil fuel based generators in many places in California

## Slide 9: Interconnection in Rural Communities
Rural Infrastructure is outdated and not properly maintained
The dispersed low numbers of electricity users creates load balancing issues
Jurisdictional issues related to line management between CAISO, PGE and POUS
Risk liability and future investment by public actors

## Slide 10: California Mid Term Reliability Needs Firm Power
Increasing procurement of firm renewables, especially dispatchable renewables, will reduce the need for more diesel backup generators that undermine the state’s climate change and air quality goals.
Numerous studies, including the modeling for SB 100 done by the CEC, have concluded that California will need significant new firm resources to meet our climate and energy reliability goals. According to modeling done for the CEC’s SB 100 report, California will need up to 15,000 megawatts of firm renewables, including a significant amount of dispatchable power.
The CPUC has called for 1,000 megawatts of new, firm renewables. The California Energy Commission has also underscored the need for more firm and dispatchable renewables in the 2021 Integrated Energy Policy Report, stating that “the intermittency of solar and wind resources necessitates flexible or dispatchable resources that can quickly come on-line when the sun sets or winds stop blowing.”
Environmental Defense Fund has issued a blog about firm power needs.
Decision 21-06-035, adopted June 24, 2021 in R.20-05-003, at page 35.
California Energy Commission, 2021 Integrated Energy Policy Report, Volume III, at page 24. Id. at page 72.

## Slide 11: Community Scale and Microgrid Use of Biomass to Electricity Procurement
Microgrid Proceeding
BioMAT
Program requires procurement of 50 MW of bioenergy from forest biomass
Under 5MW have been procured due to various factors
Program is currently offering PPA of 19.7 cents, not even an incentive at todays prices
Program set to expire January 2026
Indications that CPUC will review program this year
CCA Involvement
SB 1339, a bill enacted in 2018, directs the California Public Utilities Commission, in consultation with the California Energy Commission and California Independent System Operator, to undertake a number of activities to further develop policies related to microgrids.
The Microgrid incentive program On April 6, 2023, the Commission approved rules for the MIP for Pacific Gas and Electric Company (PG&E), Southern California Edison (SCE), and San Diego Gas & Electric (SDG&E). It allocates $79.2 million for PG&E, $83.3 million for SCE, and $17.5 million for SDG&E. Projects selected under the MIP can receive up to $15 million in award funding.
Importance of “Track 5” Energy Division Public Workshop on Stakeholder Proposals for Microgrid Multi-Property Tariffs

## Slide 12: Wrap Up; Questions?
Contact:
CLERE INC
Christiana Darlington
christiana@clereinc.net

## Slide 13: Optimizing biomass utilization: Clean fuels and carbon removal
Sam Uden – Conservation Strategy Group
26th June 2024

## Slide 14: The problem: Getting to scale
Goal: 1 million+ acres/year forest treatments
Barrier: Expensive
  $2,000/acre x 1 million acres/year = $2 billion/year (low estimate)
  Nat Resources General Fund in FY23/24 = $8 billion
Waste biomass presents an opportunity to address this barrier while driving climate and economic development benefits

## Slide 15: Science says

## Slide 16: Why clean fuels?
Not everything can or will be electrified – planes, ships, long-haul trucks, some industry
  Biomass one of the only non-fossil options for producing liquid and gaseous fuels
Clean fuels also high value – maximize value of waste and support for forest treatments
Notes: 1) Climate and energy transition argument. Demand for liquid fuels will persist through 2045 and potentially beyond in aviation, shipping, long-haul trucking etc. Non-fossil liquid fuels support economy-wide decarbonization through displacement of fossil fuels in transportation and industry.
  Approximate projected petroleum demand for 2045 = 2 billion GGE (per Scoping Plan, UCSB report)
  Conversion factor for standard gasification plant (LLNL GTN): 4,536 BDT/day = 72 million GGE/yr
  15 million BDT (1m acres/yr) = 700 million GGE
  Takeaway: Converting every scrap of forest biomass could still only serve 35% of liquid fuel demand in 2045
2) Value maximization argument. Liquid fuels are valuable products. There is a limited amount of biomass though, so focusing on waste is good. To the extent feasible, want to maximize the value to help cover the treatment cost. Fuels > power. LCFS, federal incentives, etc.
  15 BDT = 1T H2 = $2,500 ($2,000 wholesale + $525 from avoided 7tCO2e @ LCFS $75/ton)

## Slide 17: Why carbon removal?
Carbon removal has a key role in net-zero by compensating for residual emissions
Biomass a lead option for carbon removal (LLNL, others)
AB 1279: CA needs 65 Mt of carbon removal by 2045
Source: Adapted from the California Air Resources Board’s 2022 Scoping Plan Inventory Sectors Modeling Data Spreadsheet
Chart: Estimated economy-wide emissions through 2045
| 2024 | 2030 | 2045
Emissions | 332.2872 | 226.3237 | 64.838
CDR | 0 | -6.7744 | -74.9918
Notes: The 2022 Scoping Plan estimates that California will have around 65 MMT CO2e remaining in the economy in 2045.
Scoping Plan says we need 75 million tons of removal by 2045. An additional 25 million tons is expected to be removed from the industrial and electric sectors using carbon capture and sequestration technologies. We currently remove zero.
Biomass is a key pathway. Converting woody biomass residues, which have already removed carbon from the atmosphere, and capturing the carbon for permanent storage underground has the potential to remove 125 million metric tons of CO2 per year from the atmosphere by 2045 in California. Equivalent to over 30% of the state’s entire emissions portfolio.

## Slide 18: Low Carbon Fuel Standard
CARB program which provides incentives for low-carbon and carbon-negative fuels to decrease emissions in the transportation sector
Current barrier: No LCFS pathway/lifecycle assessment for forest biomass.
Key issue: what are the avoided emissions?
Cal Poly Humboldt (Kevin Fingerman) one group developing a model

## Slide 19: Renewable Fuel Standard
U.S. EPA program which provides incentives for clean fuels
Current barrier: Feedstock from majority of CA forests ineligible
Key issues:
  Federal lands ineligible;
  “Areas at risk of wildfire” an exception
Tribal lands are now considered “non-federal” under the RFS
Source: University of Wisconsin-Madison. Wildland-Urban Interface (WUI) Change 1990-2010.

## Slide 20: Inflation Reduction Act: 45V, 45Q, 40B
Notes: 45V
Available incentives ex) Huge biomass to H2 facility w/ CCS (ie 100m kg H2/yr (LLNL-ish))
  $0.60/kg H2 produced = $60 million/yr. Note: varies based on total lifecycle emissions (e.g. a facility without CCS would get $0.12/kg)
  $3.00/kg H2 produced = $300 million/yr (x5 multiplier). Based on prevailing wages, apprenticeship etc.
  Overall: Dependent on LCA and prevailing wages provisions
Eligibility
  Biomass will definitely be eligible as a feedstock. Likely to depend on lifecycle emissions accounting (e.g. will indirect land use change be considered? Counterfactuals? And how would that affect the emissions of clean H2?)
  Three pillars (ie additionality, temporal matching, deliverability) might apply for biomass -> electricity -> electrolysis.
  Overall: IRS trying to determine how to accurately capture LCA of biomass pathways
45Q
Available incentives ex) huge biomass to fuels facility w/ CCS (ie 2.1 million tons captured CO2/BDT in 1 year (LLNL))
  $17/ton CO2 captured = $35 million
  $85/ton CO2 captured (prevailing wages) = $178 million
  Overall: $/ton credit varies based on method of storage (e.g. $12/ton or $60/ton for utilization with/without prevailing wages).
40B
Available incentives ex) huge biomass to fuels facility with CCS (ie 50 million gallons SAF/yr, using biomass and CCS)
  $1.25/gallon SAF + $0.50 (maximum supplementary addition) = $1.75/gallon SAF
  Estimated annual total = $87.5 million/yr

## Slide 21: State grant and lending programs
Notes: DOC pilot program. Funding for Phase 2 cut in 2024/25 budget. Around $124k remaining for local assistance grants and administrative support (e.g. staffing, contracts etc)
Climate Catalyst Revolving Loan Fund. Direct financings could be $1million and above.
CalFIRE. 2024 funds available up to:
  $3million for biz development
  $5 million for workforce development
  $500,000 for biz R&D
  Awarded over $17 million in Q1
Clean Transportation Program. $100million annually (on average) for ZEV and H2 infrastructure, medium- and heavy-duty vehicles and workforce training. Available funding will depend on final state budget.

## Slide 22: Thank you!

## Slide 23
To sequester carbon
and leave a legacy of fertile soil

## Slide 25: CDR with Co-Benefits >25,000 research articles

## Slide 26
We modify biomass power plants to produce biochar

## Slide 27
The product ships with standard trucks

## Slide 28
We often co-locate with compost yards for processing and distribution

## Slide 29
With >6yrs of field trials, our biochar has shown improved crop yield in the farmlands of major ag companies

## Slide 30
We’ve been doing this since 2016

## Slide 31: “When the carbon is worth more in the ground than it is in the furnace…”
Vs
“…a business we might have”

## Slide 32
Farmland Improvement, Potting Media, etc.
From June 2016 till November 2020, Pacific Biochar survived (barely) on revenue from ag sales alone

## Slide 33: In 2020, Pacific Biochar registered the first carbon removal credits for biochar. Now that we can get compensated for carbon removal, this is a viable business for growth
Carbon Dioxide Removal, Voluntary Markets
Farmland Improvement, Potting Media, etc.

## Slide 34
In 2023 we delivered more durable CDR than other company on Earth!

## Slide 35: Our biochar production approach is innovative and highly efficient. We partner with existing infrastructure built for generating energy from biomass waste streams using varieties of combustion equipment.
Baseline Process: A river of combustion

## Slide 36: We then modify the machinery and operating parameters to achieve biochar production. This production of biochar requires that they add a bit more biomass on the front end to maintain the same energy output. The modifications are low-cost and simple, the net result is highly-efficient biochar production.
Change of Practice: A stream of pyrolysis within a river of combustion

## Slide 37
Humboldt Sawmill, CA, generating biochar from woody biomass waste currently.

## Slide 38
Georgia Renewable Power, GA, biochar production from woody biomass commenced Q1 2023.

## Slide 39
Honey Lake Power, CA, biochar production from TIER 1 high fire hazard biomass waste anticipated in Q2 2024

## Slide 40
Several more plants in US, in discussions for biochar production in 2024, 2025

## Slide 41
Josiah Hunt
CEO, Founder
Annie Nichols Director of Ops and Carbon
Tal Sarig
Finance
15 yrs career focus on biochar
BS in Agroecology and Env. Quality, UH Hilo
Exp with project dev and MRV for 40+ biochar producers
8 yrs managing sustainability and carbon projects
Stanford MBA, M.S Env Science.
Former COO of Israeli submarine fleet

## Slide 42
Charlie McIntosh Products Manager
Ryan Hoffman Sales and Logistics
8 yrs sales and logistics experience at major soil yard in CA
BA in Environmental Studies, UCSC
3 yrs working with PB
BS in Chemical and Biological
Engineering, UC Boulder
Licensed CA attorney since 2014
BS in Molecular Biology, UCSB
Michael Fallon General Counsel, Founder
Jim Turner
Lead Engineer
35 yrs at Sierra Pacific Industries
Led boiler QC for SPI fleet, boiler operator at Loyalton

## Slide 44
PCWA Biomass Supply Symposium | June 26th, 2024
ANEW CARBON
Reduced Emissions from Megafires Forecast Methodology
Confidential and Proprietary
www.anewclimate.com

## Slide 45
178
Employees
120+
Forest carbon projects under management
6.1+
Million acres enrolled in carbon projects
Who We Are
Largest marketer and developer of high-quality carbon offsets and environmental credits in North America
Innovator and first mover on new protocols and pathways in LCFS, RINs, Carbon
Expansive geographic reach with offices across the U.S., Canada & Europe
The most decorated firm in the industry, receiving industry awards and first place market rankings
Anew brings together climate-committed businesses and environmental projects to create measurable impact. Together, we are helping build the low-carbon economy of the future.

## Slide 46
Well Managed Forests Hold More Carbon
Carbon carrying capacity low frequency high-severity fires
Carbon carrying capacity high-frequency low-severity fires

## Slide 47
Private Plantation Timberlands

## Slide 48
Private Plantation Timberlands
Expected funding to be returned to partner over 5-year contract: $18.9-$28.3 million
(9,500 acres treated per year @ $497/acre aggregate

## Slide 49
Project Potential Across California

## Slide 50
REM Credit Demand
Primary sources of demand are entities seeking compliance with CEQA and voluntary market buyers
Chart: Tonnes of CO2-equivalent
| North American voluntary carbon demand (2023) | Average annual compliance demand (CA) | Estimated CEQA demand
 | 11800000 | 21118296 | 30000000

## Slide 51
David Lach
Director – Natural Climate Solutions
dlach@anewclimate.com
Thank you
www.anewclimate.com | 51